Mandatory Frequency Areas

Pilots must transmit the following on the appropriate frequency in, or around, a Mandatory Frequency Area or Aerodrome Traffic Frequency Area:

Arrival

- before entering the MF area, and where possible 5 minutes before entering the MF area, giving the aircraft position, altitude, estimated time of arrival at the aerodrome, and the arrival procedure intended

- on joining the circuit and position

- on downwind

- on final approach

- when clear of the runway

Departure

- intentions before entering a manoeuvring area (taxiway)

- departure intentions before moving onto the runway

- before taking-off

- departing from the circuit

- when clear of the MF area

Flying through an MFA or ATF Area

- five minutes before entering the MF area and just before entering, giving the aircraft position, altitude and pilot's intentions, and when clear of the MF area

Circuits

When flying continuous circuits - joining the downwind leg, on final with pilot's intentions and clear of the runway after landing

Note:

Pilots must remain clear of an MFA until contact with the FSS or CARS has been established.

All of these calls update your position and intentions to other aircraft and to the FSS specialist or CARS operator so that they may include you in their advisories to other aircraft and to vehicles working on the airport.

When an FSS specialist or CARS operator know your intentions, he/she will issue instructions for vehicles to clear a taxiway or runway. It is easier to see another aircraft if you know where to look. It is also important to know where IFR aircraft are in relation to the airport, especially on cloudy days. An IFR aircraft may descend out of cloud above the traffic pattern or onto final approach.

Special VFR must be requested and cleared before entering a Class "E" control zone. This clearance is issued by ATC through the FSS specialist or CARS operator. An SVFR clearance will not be issued to enter a control zone or to depart an airport with a control zone if there is an aircraft on approach or about to depart the airport.